## Slide 1: Chapter 8
Process and Capacity Analysis

## Slide 2: Process & Capacity Analysis Context
Decisions taken with respect to
  The amount of capacity that an operating unit has
  The manner in which the existing capacity is put to use
will lead to loss of productivity & overall reduction in the profitability of the operating system
Examples
  Excessive delay and waiting in service systems such as a teller counter in a bank
  Some factories working with near 100 percent utilization of their resources

## Slide 3: Issues in Process Analysis
Do I have adequate number of resources to meet the demand?
  If I need to add some extra resources where should I add?
What is the utilization of my resources?
If I need to increase the capacity of my system how should I modify the process?
  Should I add some more resources?
  What will the cost of my operation?
One can find answers to the above questions by process analysis

## Slide 4: Process Analysis Definition & Scope
Process analysis utilizes some analytical mechanism to understand the impact of
  process design on output, cost or any other performance metric
  alternative process configurations on the chosen performance metric

## Slide 5: Process Flow Charting
Design & Analysis of process begins with identification of
  activities that constitute the process
  time taken for each of the activity
  nature of flow of materials/information in the process.
A pictorial representation of all these information could be developed using process flow charting.
Process flow charting employs a set of standard symbols and graphical tools to represent all the information pertaining to the process
The symbols used are
  A step in the Process
  Transportation (Move)
  Storage or Inventory

## Slide 6: A Simplified Process Flow Chart Case of Shirt Manufacturing
Inventory of Cloth & Other materials
Spreading
Cutting
Stitching 1
Stitching 2
Assembly
Pressing &
Inspection
WIP
Inventory
Inventory of Shirts

## Slide 7: Planning Premises in Process Design
Three generic planning premises are in use in operations management
  Make-to-Stock (MTS): more amenable for systems with fewer product varieties and high production volume as in the case of continuous and streamlined flow systems
  Assemble-to-order (ATO): useful for intermittent flow systems catering to the mid-volume mid-variety situations
  Make-to-order (MTO): organizations typically belong to manufacturer of high product variety (jumbled flow process systems) use this planning methodology

## Slide 8: Capacity Planning using MTS, ATO & MTO: The case of services
Peak Hour
Assemble to order
Service Portfolio (narrow)
Demand Mgmt.
  Reservations
Exploiting
  Multi-skill labour
  Flexible work force
Non-Peak Hour
Made to order
Service Portfolio (wide)
Demand Mgmt.
  Special Tariffs, offers

## Slide 9: Process Analysis issues for MTS
From a process and capacity analysis perspective MTS is related to mass production systems. Therefore the relevant questions for process and capacity analysis are:
  What is the productive capacity of my process per shift or per day?
  Where is the bottleneck for this process?
  If I need to increase the capacity of the process at which stage of the process should I invest?
  Can I improve the productive capacity by other means than investing in new resources?

## Slide 10: Process Analysis Performance Metrics
Throughput time: Throughput time (TPUT) is the elapsed time from the first stage of the process to the last stage of the process. It is also known as lead time.
Cycle Time: Cycle time is the elapsed time between two successive output from a process that is continuously operating in a given period of time.
Bottleneck: That stage of the process that dictates the output of a process is the bottleneck.
TPUT is a relevant measure for MTO systems.
Measures such as Cycle Time and Bottleneck are relevant in the case of MTS systems.

## Slide 11: Process Analysis Toy Manufacturing (Example 8.1)
Prepare
8 minutes
Pre-treat
12 minutes
Paint
20 minutes
Dry
45minutes
Inspect &
Pack
5 minutes
The throughput time for the process is 55 minutes
The spray painting is the bottleneck in the process
Cycle time is 20 minutes. The implication of this is that when the process operates in a continuous manner, a pallet of finished toys come out every 20 minutes.

## Slide 12: Process Analysis (Example 8.1) A graphical representation with start and end times
Every batch of four toys come out exactly in an interval of 20 minutes which is the cycle time for the process

## Slide 13: Process Analysis (Example 8.1) Production Capacity of the system
Prepare
7.5 pallets/hr
Pre-treat
5 pallets/hr
Paint
3 pallets/hr
Dry
Inspect &
Pack
12 pallets/hr
The system can produce at the rate of 3 pallets per hour (12 toys)
For a 8 hour operation the daily production is 24 pallets (72 toys)
Capacity is unbalanced across different stages of the process

## Slide 14: Production Capacity under varying batch sizes (Example 8.2)
Prepare
(8 minutes)
7.5 pallets/hr
Pre-treat
(12 minutes)
5 pallets/hr
Paint
(20 minutes)
3 pallets/hr
Dry
Inspect &
Pack
(5 minutes)
12 pallets/hr
Existing Scenario: Batch Size of the Process = 1 pallet
Scenario 1: Batch Size of the Process = 2 pallets
Prepare
(4+ (2*4) =
12 minutes)
10 pallets/hr
Pre-treat
(12 minutes)
5 pallets/hr
Paint
(20 minutes)
6 pallets/hr
Dry
Inspect &
Pack
(5 minutes)
12 pallets/hr
Scenario 2: Batch Size of the Process = 3 pallets
Prepare
(4+ (3*4) =
16 minutes)
11.25 pallets/hr
Pre-treat
(12 minutes)
5 pallets/hr
Paint
(20 minutes)
9 pallets/hr
Dry
Inspect &
Pack
(5 minutes)
12 pallets/hr

## Slide 15: Production Capacity under varying resource availability (Example 8.2)
Scenario 1: Batch Size of the Process = 3 pallets, 2 pre-treatment units
Prepare
(4+ (3*4) =
16 minutes)
11.25 pallets/hr
Paint
(20 minutes)
9 pallets/hr
Pre-treat
(12 minutes)
5 pallets/hr
Dry
Inspect &
Pack
(5 minutes)
12 pallets/hr
Prepare
(8 minutes)
7.5 pallets/hr
Pre-treat
(12 minutes)
5 pallets/hr
Paint
(20 minutes)
3 pallets/hr
Dry
Inspect &
Pack
(5 minutes)
12 pallets/hr
Existing Scenario: Batch Size of the Process = 1 pallet, 1 painting booth
Pre-treat
(12 minutes)
5 pallets/hr

## Slide 16: Process Analysis (Example 8.2) Some important observations
Batch sizes play a crucial role in determining the bottleneck of a process
As several choices are made with respect to the resources and batch size bottleneck shifts from one stage of the process to another. This is referred to as wandering bottleneck.
A process analysis exercise often leads to the issue of improving the process

## Slide 17: Business Process Engineering Some guidelines to identify scope
Extensive information exchange, data redundancy and re-keying of data points to arbitrary fragmentation of a natural process
Large investment in inventory, buffers and other assets indicates that the existing process is unable to cope up with uncertainty
High proportion of checking, control and progress monitoring implies too much fragmentation of the process
Inadequate feedback in the process results in excessive rework and iteration
Increase in complexity of operations, exceptions and special cases also indicate the need for simplifying the process by revisiting the process fundamentals

## Slide 18: Components of Lead Time in Organizations
Actual Operations
Time
Lost Time
(Scrap, Rework,
Unnecessary Activities)
Moving Time
Between Processing Units, People across Departments
Waiting Time
Unclear Instructions, Missing Information, Approvals, Authorizations,
Non-availability of Material & Components, Resources
Awaiting Approvals, Decisions
Time lost in coordination among chain of customers

## Slide 19: Implementing BPR A three-step methodology
Understand
the existing
Process
Simplify the
Process by
eliminating NVA
Automate
the Process
Process Mapping
Brainstorming
“As-is” analysis
NVA Analysis
“Should-be”
analysis
EDI
ERP
Internet tools
Tools used in each step

## Slide 20: Process or Value Stream Mapping Some alternatives…
Customer order “walk through”
Collaborative brainstorming/charting
Bottom-up approach – Interviews of staff in functional departments
Executive judgment

## Slide 21: Process Improvement NVA Analysis
Categorize activities
  Value Added (VA)
  Non-value added (NVA)
  Necessary but non-value added (NNVA)
Obtain measures to assess the process
  Distance, Time, Staff deployed, categories of NVA
Brainstorm improvement opportunities
  Low hanging fruits
  Medium term solutions
  Longer term solutions

## Slide 22: Process Mapping Study A Summary of outcome
Category of Activity | No. of activities | Time (Hours) | % of Total Time
Waiting | 53 | 1098 | 65.4
Moving | 18 | 373 | 22.2
Adding Value | 5 | 106 | 6.3
Adding Cost | 5 | 104 | 6.1
Total | 81 | 1680 | 100.0

## Slide 23: Capacity Planning
Capacity denotes in general the extent of availability of these resources for use by various processes
It also denotes the maximum output of products and services one can achieve using these resources
Capacity planning is a systematic approach to
  Estimate the amount of capacity required,
  Evaluation of alternative methods of augmenting capacity
  Devise methods to use capacity effectively
Capacity planning is important
  It has a significant impact on the cost of operation of the system due to large fixed costs associated with capacity
Economies of scale is an concept in economics related to capacity

## Slide 24: Economies of Scale An illustration
2000 units
per month
5000 units
per month
10,000 units
per month
Units of output
Average unit cost of output

## Slide 25: Capacity buildup Alternative modes
Capacity
Demand
Typical mode
Proactive mode
Reactive mode
Time

## Slide 26: Video Insight 8.1 Capacity Planning in Melbourne Rail Network
Right click on the URL below to open the hyperlink in the web browser…
https://www.youtube.com/watch?v=CQ2IGZYTTNw

## Slide 27: Input measures of capacity
Firms operating in low volume, high variety situation find it relevant
  Refining capacity of BPCL refinery in Mumbai is 260,000 barrels of crude per day
  Television manufacturer often measures its capacity by millions of picture tubes that it produces
  Tool room facility will measure its capacity in terms of machine hours
  A hospital will measure the capacity in terms of number of beds.

## Slide 28: Output measures of capacity
When the volume of production is high and the variety is relatively low output measures are useful
  Toyota Kirloskar Auto Parts measures it capacity in terms of number of transmission gear boxes it can produce
  Tata Bearings, a division of Tata Steel, has a capacity of 25 million pieces per annum
  MICO Bosch has an installed capacity of one lakh distributor pumps at its Jaipur plant
  An automated car wash facility’s capacity can be measured in terms of number of cars serviced per day

## Slide 29: Japanese notion of capacity
Capacity = Work + Waste
Nine types of waste according to Canon production system:
  Waste in Operations
  Waste in Startup
  Waste in Equipment
  Waste in Defects
  Waste in Materials
  Waste in Indirect Labour
  Waste in Human Resources
  Waste in expense

## Slide 30: Nine Source of Waste An illustration (Ideas at work 8.2)
Source of waste | Amount (in INR million) | 
Waste due to human resources |  | 1.96
Waste due to materials |  | 21.53
Waste due to operations |  | 1.47
Waste due to start up |  | 5.24
Waste due to equipment |  | 12.90
Under utilisation of machines | 9.75 | 
Unused machine capacity | 2.50 | 
Not maintaining specifications | 0.65 | 
Total of the above |  | 43.10
Divisional turnover |  | 135.92
Waste as a percent of turnover |  | 31.70%

## Slide 31: Capacity Planning Time Horizon
Criterion | Time Horizon for planning |  | 
 | Long term | Medium term | Short-term
Time frame | 2 - 5 years | Typically 1 year | 1 week to 3 months
Planning premise | Augmenting capacity for projected growth | Balancing demand - supply | Maximising availability; Efficent use of resources
Key decisions made | Capacity Augmentation; Capital Budgeting Exercises | Adjusting demand and supply attributes to balance available capacity to requirement | Resource deployment strategies, Maintenance routines, Improvement projects to be undertaken
Tools & Techniques used | Investment planning; Break-even analysis, Discounted cash flow techniques; Decision Trees | Aggregate Production Planning; Make or Buy | Planning & Scheduling, Total Productive Maintenance, Waste elimination by continuous improvement; Simulation; Heuristics; Waiting line models

## Slide 32: Capacity Planning Framework
Step 1
Estimating the capacity requirements for the planning Horizon
Step 2
Computing the available capacity
Estimating the quantum of capacity to be augmented
Step 3
Identifying the available alternatives
Selecting the best one for capacity augmentation

## Slide 33: Capacity Planning Computational steps
Step 1: Estimate the total requirement for the planning horizon
Step 2: Estimate Labour and Machine requirements
Step 3: Compute Capacity Availability
Step 4: Compare availability with Requirement
Step 5: Evaluate alternative methods for capacity augmentation

## Slide 34: Capacity requirements
Projected demand per unit time during the planning horizon = D
Standard labour hours required per unit of product = SL
Efficiency of labour = EL
Capacity requirements (Labour) =
Capacity requirements (Machine) =

## Slide 35: Capacity Availability
System availability
  Number of working days in the planning horizon: Nd
  Number of working hours per day: h
  System availability (Hours) = Nd * h
Resource availability
  Number of machines available: Nm
  Machine: Time lost in breakdowns & maintenance = b %
  Number of workers available: NL
  Labour: Absenteeism of the workers = a %
Capacity available in the system (Hours)
  Machine: Nd * h * Nm * (1 – b/100)
  Labour: Nd * h * NL * (1 – a/100)

## Slide 36: Capacity Augmentation Alternatives
Waste Elimination
Multi-skilling of workforce
Sub-contracting/Outsourcing
De-bottlenecking
Addition of new capacity

## Slide 37: Example 8.5
A product is manufactured in a shop using a five-stage process. The first step in the process is to cut the sheet metal to required shapes and sizes using a shearing process. After the shearing process, the components are subjected to pressing operations to alter the shape of the flat sheet as per the design. In the third stage of the process welding is done to join the components. The next step in the process is a painting operation. After painting, the components are packed and kept ready for dispatch.
The time take for each of these operations are 20, 30, 15, 12 and 6 minutes respectively.
Presently, each stage has only one machine for operation.
Map the process and analyse the capacity with respect to the following scenarios:
  If the shop works for an 8-hour shift with an effective available time of 450 minutes, what is the production capacity of the shop?
  Where is the bottleneck in the system? If we want to add one machine, where should we make the investment?
  Identify the additional capacity required for a daily production target of 25 units. Compute the utilisation of the machines as per the revised capacity calculations.

## Slide 38: Solution to example 8.5
The production capacities are:
  Shearing: 450/20 = 22.50 Pressing: 450/30 = 15.00
  Welding: 450/15 = 30.00 Painting: 450/12 = 37.50
  Packing: 450/6 = 75.00
The smallest number in the above calculation limits the production capacity for the shop. Therefore, the current production capacity is 15 units per day.
Shearing (20 minutes)
Pressing (30 minutes)
Welding (15 minutes)
Painting (12 minutes)
Packing (6 minutes)
Shearing (20 minutes)
Pressing (30 minutes)
Welding (15 minutes)
Painting (12 minutes)
Packing (6 minutes)
Pressing (30 minutes)
Bottleneck

## Slide 39: Solution to example 8.5
The production target is 25 per day now. Since a day has 450 minutes, the maximum time that the process can take in each stage is 18 minutes.
  Packing, Painting and Welding sections have timings less than 18. Therefore, they do not need any more investment in capacity.
  By adding one more machine at the pressing stage, the effective time will be less than 18 minutes.
  Similarly, by adding one more machine at the shearing stage, the effective time will be 10 minutes.
  Utilisation of Shearing =
  Utilisation of Pressing =
  Utilisation of Welding =
  Utilisation of Painting = 66.67% Utilisation of Packing = 33.33%

## Slide 40: Bottleneck & Capacity Analysis The Wandering Bottleneck
Shearing (20 minutes)
Pressing (30 minutes)
Welding (15 minutes)
Painting (12 minutes)
Packing (6 minutes)
Shearing (20 minutes)
Pressing (30 minutes)
Welding (15 minutes)
Painting (12 minutes)
Packing (6 minutes)
Pressing (30 minutes)

## Slide 41: Hierarchies in Capacity Estimation
First operation
Fabrication Shop
Paint Shop
Electrical & Wiring
Assembly & Testing
Shearing Unit
Pressing Unit
Welding Unit
CNC Turret Press
Hydraulic Press
NC Press Brake
63 Tonne ECC Press
Denotes bottleneck
in the process

## Slide 42: Capacity Planning Decision tree analysis (Example 8.6)
1
A
Add new
capacity
Go for
Sub-contracting
Expand
B
C
Demand High
Demand High
2
Demand High
Add new capacity
Demand Moderate
Demand Moderate
Demand Moderate
Continue with
sub-contracting
(Rs. 750,000)
(Rs. 275,000)
(Rs. 787,500)
Revenue: Rs. 400,000 per year
Revenue: Rs. 850,000 per year
Revenue: Rs. 200,000 per year
Revenue: Rs. 450,000 per year
Revenue: Rs. 180,000 per year
Revenue: Rs. 350,000 per year
Revenue: Rs. 850,000 per year
Denotes the best option
at each decision point

## Slide 43: Solution to Example 8.6
Decision point 2
Revenue from adding new capacity = Rs. 850,000 x 4 = Rs. 34,00,000.00
Cost of adding new capacity = Rs. 7,87,500.00
Net revenue from this option = Rs. 26,12,500.00
Revenue from sub-contracting option= Rs. 350,000 x 4 = Rs. 14,00,000.00
Therefore the best option at this stage is to go for adding new capacity
Node A
Revenue in the case of high demand = Rs. 850,000 x 5 = Rs. 42,50,000.00
Revenue (moderate demand) = Rs. 400,000 x 5 = Rs. 20,00,000.00
Expected revenue at node A
E[A] = (42,50,000 * 0.40 + 20,00,000 * 0.60) = Rs. 29,00,000.00
Cost of adding new capacity = Rs. 7,50,000.00
Net revenue from this option = Rs. 21,50,000.00

## Slide 44: Solution to Example 8.6
Node B
Revenue in the case of high demand = Rs. 550,000 x 5 = Rs. 27,50,000.00
Revenue (moderate demand) = Rs. 300,000 x 5 = Rs. 15,00,000.00
Expected revenue at node B
E[B] = (27,50,000 * 0.40 + 15,00,000 * 0.60) = Rs. 20,00,000.00
Cost of expanding the capacity = Rs. 2,75,000.00
Net revenue from this option = Rs. 17,25,000.00
Node C
In the case of high demand, it is better to add new capacity after I year than continuing with the sub-contracting option. This will fetch a net revenue of Rs. 26,12,500.00 during the last four years. Moreover, in the first year, it would have fetched a revenue of Rs. 3,50,000.00. Therefore,
Revenue in the case of high demand = Rs. 29,62,500.00
Revenue (moderate demand) = Rs. 180,000 x 5 = Rs. 9,00,000.00
Expected revenue at node C
E[C] = (29,62,500 * 0.40 + 9,00,000 * 0.60) = Rs. 17,05,000.00
Cost of sub-contracting is none.
Net revenue from this option = Rs. 17,05,000.00

## Slide 45: Capacity Planning Chapter Highlights
Process analysis is the mechanism to understand the impact of the process design on output, cost or any other performance metric using some analytical tools
A pictorial representation of all process related information could be developed using process flow charting
Process flow charting employs a set of standard symbols and graphical tools to represent all the information pertaining to the process
Three generic planning premises are in use in operations management: make-to-stock, make-to-order and assemble-to-order

## Slide 46: Capacity Planning Chapter Highlights…
The basic approach to planning in made-to stock system is to schedule production for the purpose of replenishing stock to some predetermined level
MTO planning methodology is used by organizations that manufactures high product variety in low volumes
Organizations use input and output based measures for defining capacity
  High volume low variety manufacturers use output bases measures for defining capacity.
Capacity = Work + Waste. Therefore, one way of augmenting capacity in organizations is to eliminate waste from the system.

## Slide 47: Capacity Planning Chapter Highlights…
The capacity planning framework changes with the time horizon
  The emphasis in the short term is to maximize capacity availability through efficient use of resources.
  On the other hand, in the medium term the emphasis is on matching the supply with the demand on a period by period basis.
The capacity planning framework consists of a three step process:
  Estimate the capacity requirement for the planning horizon
  Identify the quantum of capacity to be augmented
  Select an appropriate alternative for capacity augmentation
Selection of an appropriate alternative for capacity augmentation could be done using a decision tree model