## Slide 1: Chapter 9
Design of Manufacturing Processes

## Slide 2: Factors Influencing Process Choices
Volume: Average quantity of the products produced in a manufacturing system
  Low volume: Turnkey project management firms such as L&T and BHEL
  High volume: Consumer non-durable and FMCG sector firms, Automobile, Chemical Processing
  Mid-volume: Consumer durables, white goods and several industrial products
Variety: Number of alternative products and variants of each product that is offered by a manufacturing system
  Variety of product offerings is likely to introduce variety at various processes in the system; alternative production resources, materials, and skill of workers
Flow: Flow indicates the nature and intensity of activities involved in conversion of components and material from raw material stage to finished goods stage

## Slide 3: Relationship between Volume & Variety
High Volume
High Variety
Mass Production
Petrochemicals,
Automobile
FMCGs
Consumer non-durables
Project Organizations
Power plants
Aircraft manufacturing
Bridges & Large
Constructions
Motor Manufacturing
Pharmaceuticals
White Goods
Consumer Durables
Mid-volume
Mid-variety

## Slide 4: Processes & Operations Systems Available Alternatives
Process characteristics are largely determined by the flow of products in the operating system
Three types of flows occur in operating systems:
  Continuous
  Intermittent
  Jumbled

## Slide 5: Continuous Flow System
Characterized by a streamlined flow of products in the operating system
Conversion process begins with input of raw material at one end, progresses through the system in an orderly fashion to finally become finished goods at the final stage
Production process is sequential and the required resources are organized in stages
  Examples:
    several chemical processing industries such as manufacture of petrochemicals, steel, pharmaceutical, cement and glass
    In a discrete manufacturing industry high volume production of very few varieties (such as electrical bulbs or spark plugs)

## Slide 6: Paper Manufacturing An example of process industry
Logs and chips
of wood stored
Crushing of
logs and chips
Processing of
the wood
Cleaning &
Bleaching
Refining the
Wood pulp
Drying the
wood pulp
Stretching
Paper rolling
Cutting
Final packing
Paper making
Pulp making
Preparatory

## Slide 7: Process Industry Distinctive features
There should be balance of capacity between all the stages in the manufacturing process to maintain an even flow of the material from the raw material stage to finished goods
Productivity of the system is directly related to the flow rate (or throughput) of the product
Requires huge capital investments, as incremental addition at a later stage not possible. High productivity implies lower cost of production and vice versa.
Need to make continuous process improvements and capacity de-bottlenecking to maximize the flow rate in the system
Failure of any intermediate stage in the system will have an adverse effect on the cost (see Ideas at work 9.2 for an illustration of this)

## Slide 8
Oil & Gas Exploration & Production
Refining & Marketing
LPG
Naptha
Gasoline
ATF
Kerosene
Diesel
Sulphur
Fuel Oil
Bitumen
Cracker
Fuel Gas
Ethylene
C4s
Propylene
Toluene
Xylene
Benzene
Salt
Caustic Unit
EDC
VCM
PVC
Poly Propylene
MEG
EO
Oxygen
Polyethylene
LAB
N-Parafins
PFY
PSF
Polyester resin
Polyester chips
Texturised Yarn
Spun Yarn
Fabric
Wool, Silk
Retailing
Textiles
Polymers
& Chemicals
Refining
Oil & Gas
PG Complex
PTA
PX
Hazira
Complex
Jamnagar
Complex
Bombay
High
Naroda
Complex
Backward Integration at Reliance

## Slide 9: Operations Management Issues Process Industry
The notion of capacity
  Flow rate determines capacity
  Bottleneck easily identifiable
Nature of inventories
  Work in Progress will be minimal
  Inventory of Spares & Maintenance will be high
Importance of maintenance
Relevance of vertical integration
  Joint & Bye Products are many
  Exploiting processing opportunities of these important

## Slide 10: Video Insight 9.1 Manufacturing of Sugar & Apparels
Right click on the URL below to open the hyperlink in the web browser…
Plant tour to understand how Sugar is being manufactured https://www.youtube.com/watch?v=R9J7pOU5FSg#aid=P9Ci8i1FfNA
A modern apparel manufacturing unit: Best & Crompton Apparels http://www.youtube.com/watch?v=HxGLdTARCMk#aid=P8YcoLTqiEA

## Slide 11: Continuous Flow System Mass production in discrete manufacturing
In discrete manufacturing various components are manufactured in discrete fashion and the final product is obtained through an assembly process
In a mass production system, the volume of production is very high and the number of variations in the final product is low
  Examples:
    Automobile and two wheeler manufacturers,
    Manufacturers of electrical components such as switches and health care products such as disposable syringes
The entire manufacturing is organised by arranging the resources one after the other as per the manufacturing sequence (known as product line structure)

## Slide 12: Process Design for Mass Production Systems
Pre manufacturing Activities
Machining
Fabrication
Assembly
Testing
Dedicated & Decentralised Manufacturing Support
Machining
Fabrication
Assembly
Testing
Machining
Fabrication
Assembly
Testing
Product A
Product B
Product C
Machine 1
Machine 2
Machine 3
Machine m
. . .
Product A

## Slide 13: Video Insight 9.2 Manufacturing of Honda Amaze & Benz C Class
Right click on the URL below to open the hyperlink in the web browser…
Honda manufacturing plant in Tapukara India https://www.youtube.com/watch?v=A4Ar8ZLnZU0
Manufacture of Mercedes Benz C Class Cars http://www.youtube.com/watch?v=r5xmVPr8Aa8

## Slide 14: Intermittent Flow System
Characterised by mid-volume, mid-variety products/services
Increases the flow complexities
Flow and capacity balancing are difficult but important
  Process industries use batch production methods
  Discrete industries use alternative methods of designing layout issues
Capacity Estimation is hard
Production Planning & Control is complex

## Slide 15: Process Design for Intermittent Flow in Discrete Manufacturing
Pre-manufacturing activities
Gear
Components
Prismatic
Components
Other
rotating parts
Sheet
Metal parts
Housings
Shafts
Assembly & Test Assembly & Test Assembly & Test
Product A Product B Product C
Dedicated Manufacturing Support for the products

## Slide 16: Layout redesign to minimise complexity in Intermittent flow An example (Ideas at Work 9.3)

## Slide 17: Intermittent Flow System Sources of Problems
A bad choice on structure & people issues
Leads to
Complicated Material & Information Flows
Thereby
Making Production Planning & Control Complex
Which Demands
Special mechanisms to bring order out of chaos

## Slide 18: Special Mechanisms To bring order out of Chaos
Lot of paper work
Enormous supervision/Co-ordination
Progress Chasing/Expedition
All these finally result in
Long Lead Times/Poor Delivery Reliability
Excess and Unwanted Inventory
High Overhead/High Cost

## Slide 19: Jumbled Flow System
Occurs on account of non-standard and complex flow patterns characteristic in certain systems
  Highly customised items
  customer orders for one or a few
Examples
  turnkey project executor such as BHEL or L&T
  customised manufacturing systems such as PCB fabricators, sheet metal fabricators, tool room operators and printing and publishing
Operational complexity arising out of jumbled flow is high
Discrete manufacturing with Jumbled flow uses a Job Shop structure

## Slide 20: Process flow in Job Shops
Machine 1
Machine 2
Machine 3
Machine 6
Machine 5
Machine 4
Machine 7
Job 1
Job 2
Job 3

## Slide 21: Jumbled Flow System
Complex issue is capacity management
  Considerable time is lost due to repeated setup of processes
Due to jumbled flow, crisscrossing of jobs in the system results in poor visibility.
  Problems are often hidden and build up of work in process inventory takes place
Cost accounting and estimation systems are crucial as there is a constant need to quote for specific customer orders

## Slide 22: Process design for operations Salient features of alternative choices
Flow Characteristics | Continuous | Intermittent | Jumbled
Product Characteristics | High Volume, Very low variety | Mid volume, Mid variety | Very high variety, low volume
Examples of production systems | Process Industry, Mass production systems in discrete manufacturing | Batch production in Process and discrete manufacturing | Project Organisations, Tool Rooms, General purpose fabricators
Issues of importance | Flow Balancing, Maintenance, Capacity utilization and debottlenecking, Vertical integration | Manufacturing system and layout design, Changeover management, Capacity planning and estimation | Capacity Estimation, Scheduling, Production Control, Cost estimation
Operations Management Tools & Techniques | Line Balancing, Maintenance management, Process optimisation, Product layout design, Flow shope scheduling, Pull type scheduling, Single piece flow design | Forecasting, Capacity Planning and estimation, Optimized production planning and product sequencing, Group Technology layout design, Materials Management | Project Management & Scheduling, Capacity planning and optimization, Job shop scheduling, Functional Layout design, Job order costing, Work in Process Management

## Slide 23: Product – Process Matrix
Low Volume
Low Standardisation
One of a kind
Multiple Products
Low Volume
Few Major Products
Higher Volume
High Volume
High Standardisation
Commodity Products
Continuous
Flow
Connected Line
Flow (Assembly
Line)
Disconnected
Line Flow
(Batch)
Jumbled
Flow
(Job Shop)
Satellite Launch
Vehicle
Machine Tools
Auto electric
parts
Polyethylene
None
None
Source: Adapted from Hayes, R.H. and Wheelright, S.C., (1979), “Link manufacturing process and product life cycles”, Harvard Business Review, 57 (1), 133 – 140.

## Slide 24: Layout Planning
Layout planning in manufacturing & service organisations
  deals with physical arrangement of various resources that are available in the system
  with an objective to improve the performance of the operating system
Benefits of good layout design
  Jobs in a manufacturing system travel lesser distance
  Customers spend less time in service systems
  Costs & Lead time come down
  Improved quality

## Slide 25: Types of Layout
Process Layout
  arrangement of resources on the basis of the process characteristics of the resources available
Product Layout
  order in which the resources are placed follow exactly the visitation sequence dictated by a product
Group Technology (GT) Layout
  seeks to exploit commonality in manufacturing and uses this as the basis for grouping components and resources
Fixed Position Layout
  emphasis is not so much on optimum position of resources required for the process, since the product itself largely dictates this; the focus is on gaining better control of material flow and reducing delays

## Slide 26: Volume – Variety – Flow Implications for layout planning
 | Variety |  |  | 
 | Very low variety | Medium Variety | High Variety | One off execution
Flow attributes | Stream lined flow | Multiple flow paths | Dis-organised flow | Jumbled flow
Volume attributes | High Volume | Mid-volume | Low volume | One piece
Examples of operating systems | Process industry; Mass Product/ Service provider | Batch Manufacturing firms | Job shops; Customized Product/ Service Provider | Project Shops
Types of layout used | Line Layout; Product Layout | Group Technology Layout | Process Layout | Fixed Position Layout

## Slide 27: Process Layout An example
L
L
L
L
M
M
M
M
D
D
D
D
D
D
G
G
G
L
L
L
L
Product A
Product C
Product B

## Slide 28: Product Layout An example
L
L
M
D
G
L
M
D
G
L
L
D
G
Product C
Product A
Product B

## Slide 29: Alternative Layouts An example from Banking
Bank A
Bank B

## Slide 30: Product & Process Layout Pros & Cons
 | Process Layout | Product Layout
Advantages | Sharing of specialized and costly equipments | Standardised product/ process routing
 | More flexibility | Operational Control is simpler
 | Less vulnerable to breakdowns | High output rate is possible
Disadvantages | Large Inventory buildup | Low tolerance for breakdowns
 | Operational control difficult | Duplication of equipments leading to high cost
 | Excess Material Handling | Less flexibility due to dedication of resources

## Slide 31: Group Technology Layout An example
L
L
L
L
M
M
M
M
D
D
D
D
D
D
G
G
G
L
L
L
L
Cell 1
Cell 2
Cell 3
Cell 4

## Slide 32: Fixed Position Layout Example from Thermax

## Slide 33: Layout Design Performance implications
* The total distance travelled includes only those of the items manufactured on the shop floor. The number of items that finally get assembled into the final product includes many bought out items in addition to these.

## Slide 34: Layout Design Performance Measures
Performance Measure | Basis for measurement
Distance travelled by jobs in the shop floor | Kg - Metres of job movement for each product
Space utilization index | Minimum space required to actual space utilised
Material Handling costs | Rupees per month
Lead time of the processes | Hours per average product
Investment in work-in-progress | Rupees per month
Inter-departmental moves | Number and quantum of inter-departmental moves
Utilisation of the resources | Percent to total capacity
Ease of production control | Number of job cards and control documents generated; Size of the progress chasing staff
Number of ownership changes | Number of times the responsibility for the job changes hands

## Slide 35: Design of Process Layouts Alternatives
Qualitative Method
  Links some criteria to the closeness required between a pair of resources
  Computer packages such as ALDEP and CORELAP are available
Quantitative Method
  Uses some quantitative performance measures for assessing the impact of a layout design
  Seeks to arrive at the best layout design by optimising on this performance measure
  One of the popular method used in CRAFT
Performance evaluation models using computer simulation techniques

## Slide 36: Design of process layouts Qualitative method
Department 1
Department 2
Department 3
Department 4
Department 5
Department 6
O
U
A
U
O
A
O
U
O
I
X
O
E
U
A

## Slide 37: Design of Process Layout Quantitative Method
Cij = Cost per unit of transporting a unit distance from department “i” to department “j”
Fij = Inter-departmental flow between department “i” and department “j”
Dij = Distance between department “i” and department “j”
n = Number of departments to be laid out
The total cost of the plan is given by:
One can model the above as a mathematical programming problem with the objective function of minimising the total cost of the plan

## Slide 38: Design of Product Layout
Several Mass Production Systems are in operation today
  Various sub-assemblies in a mass producer need to be configured to match the production rate
  Similarly, the final assembly stations also need to have the required number of resources at each station to meet the targeted demand
A product layout design
  seeks to identify the minimum number of resources required to meet a targeted production rate and the order in which these resources are to be arranged
  Technique employed for designing of product layout is known as line balancing

## Slide 39: Line Balancing Decisions & Trade-offs
Line balancing
  A method by which the tasks are optimally combined without violating precedence constraints and a certain number of workstations designed to complete the tasks
  Key decision variables are production rate, cycle time and the number of workstations, which are inter-related
  Solving the “line balancing” problem calls for striking the right trade-off between increased production and better utilisation of resources
Cycle time is the ratio of the available time to the actual (desired) production rate

## Slide 40: Line Balancing Some measures of interest

## Slide 41: Example 9.1.
A factory working in 2 shifts each of 8 hours produces 24,000 electric bulbs using a set of workstations. Using this information compute the actual cycle time of the plant operation.
There are 8 tasks required to manufacture the bulb. The sum of all task times is equal to 12 seconds. How many workstations are required to maintain this level of production if combining of tasks into that many workstations is a feasible alternative?

## Slide 42: Solution to example 9.1.
Available time = 2*8*60*60 = 57,600 seconds
Actual production = 24,000 electric bulbs
Therefore, using equation 9.2
Cycle time for each bulb is seconds
This means that the factory is producing a bulb every 2.4 seconds.
No. of work stations required =
Therefore the tasks are to be split among the five stations such that each workstation will have sum of the task times to be 2.4 seconds.

## Slide 43: Example 9.2.
A computer manufacturer needs to design the assembly stations in the factory where the cabinet housing the hard disk, motherboard and other accessories are to be done. The factory currently works for one shift of 8 hours. The tasks, their duration and their precedence relationships are given below:
If the cycle time is 80 seconds, what will be the daily production of cabinets?
If the desired production rate is 320 cabinets per day, what is the maximum permissible cycle time?
What is the maximum and minimum number of workstations required to maintain this daily production rate?
Design an assembly setup with 5 workstations and 6 workstations.

## Slide 44: Solution to example 9.2.
Total available time per day = 8*60*60 = 28,800 seconds
If the cycle time is 80 seconds, then
Daily production rate =
Since the desired production rate is only 320 cabinets, one can obtain the maximum permissible cycle time for the assembly stations
Maximum Cycle Time =
Minimum number of workstations is dictated by the maximum cycle time permissible
Sum of all task times = 380 seconds
Minimum number of workstations =

## Slide 45: Solution to example 9.2. Design with 5 work stations
We assign tasks to the five workstations on the basis of the following two criteria:
  Workstation times should not exceed maximum permissible cycle time of 90 seconds
  The precedence relationships need to be honoured
  Average Utilisation =

## Slide 46: Solution to example 9.2. Design with 6 work stations
 | Work station 1 | Work station 2 | Work station 3 | Work station 4 | Work station 5 | Work station 6
Tasks Assigned | A | B | C,D | E,F | G | H
Workstation Times | 70 | 80 | 60 | 70 | 50 | 50
Cycle time | 80 | 80 | 80 | 80 | 80 | 80
Workstation idle time | 10 | 0 | 20 | 10 | 30 | 30
Workstation utilisation | 87.5% | 100% | 75% | 87.5% | 62.5% | 62.5%
Average Utilisation =

## Slide 47: Design of GT Layout Guiding Principles
The objective is one of sub-dividing an universe of machines and components into sub-groups
  Each sub-group of components form a part family and is endowed with a corresponding sub-group of machines known as machine groups
  Each sub-group is referred to as a cell
GT layout design is done with a systematic analysis of a machine-component incident matrix
Number of methods available for identifying sub-groups
  Production Flow Analysis (PFA)
  Clustering techniques
  Matrix manipulation methods
  Graph theory
  Mathematical programming methods

## Slide 48: Machine – Component Incident Matrix Before Grouping
Machines
Components

## Slide 49: Machine – Component Incident Matrix After Grouping
Machines
Components

## Slide 50: One man multiple machine layout An example from Lucas TVS
Press
Lathe
4 way
Drill
SS
Drill
Bench



Press
Lathe
4 way
Drill
SS
Drill
Bench

Source: N Ravichandran, “A Journey Toward Manufacturing Excellence” CII Quality Summit 2000, 61 – 115.
Old Layout
Revised Layout

## Slide 51: Flexible Manufacturing System Definition
A Flexible Manufacturing Systems (FMS) is
  A system consisting usually of numerical control (NC) machines
  Connected by an automated material handling system.
  Operated under a central computer control
  Capable of simultaneously processing a family of parts with low to medium demand, different process cycles and operation sequences
It is an attempt to solve the process complexities arising out of mid-volume and mid-variety parts

## Slide 52: Typical Machines used in FMS

## Slide 53: Structure of an FMS

## Slide 54: Flexibilities in FMS
Machine flexibility: the ease of making changes required to produce a given set of part types
Process flexibility or mix flexibility: the ability to produce a given set of part types, each possibly using different materials in several ways
Product flexibility: the ability to produce a new set of products very economically and quickly
Routing flexibility: is the ability to handle breakdowns and to continue processing the given set of part types
Volume flexibility: is a measure of the ability to operate an FMS profitably at different production volumes
Expansion flexibility: is the capability of building a system, and expanding it as need arises, easily and in a modular fashion

## Slide 55: Material Handling in FMSs
An automated storage system is used for large scale bulk storage as well as for small in line buffer storage
  Automated Storage and Retrieval System (AS/RS)
  Horizontal & Vertical Carousels
An automated transport system is used to move parts and products from the storage systems to the production operations
  Automated Guided Vehicle (AGV) system
  Conveyors in a wide variety of forms such as overhead, monorail, carry and free, power and free and under floor drag chain
  Gantry and Pick & Place Robots

## Slide 56: Factors affecting the complexity of Operations Management
Moderate Complexity
High Complexity
Low Complexity
Moderate Complexity
Variety
Low
High
No. of Stages
Few
Many
Flow
Streamlined
Jumbled

## Slide 57: Design of Manufacturing Processes Chapter Highlights
Volume, variety and flow exert significant influence on process design in organizations.
Process industries and mass production systems generally have a streamlined flow of products.
Mid-volume and mid-variety manufacturing systems have intermittent flow. Capacity estimation is difficult in such systems compared to a continuous flow systems.
Project organizations & customized manufacturing systems have jumbled flow. Capacity estimation and scheduling of jobs are quite difficult. Operations management complexity is high in jumbled flow systems.
A process – product matrix depicts the relationship between process flow characteristics and volume of production in any manufacturing organization.

## Slide 58: Design of Manufacturing Processes Chapter Highlights…
Volume, variety and flow exert significant influence on the layout problem in organizations.
  Product layouts are useful for high volume – low variety situations.
  At the other extreme, fixed position and project layouts are useful for high variety situations.
Product layout and process layouts are used in discrete manufacturing industry. They have several advantages and disadvantages.
Mid-volume and mid-variety manufacturing systems can benefit from a Group Technology (GT) layout.
Several computer packages are available for designing process layouts. Popular among them include CORELAP, ALDEP COFAD and CRAFT.

## Slide 59: Design of Manufacturing Processes Chapter Highlights…
Product layout design seeks to identify the minimum number of resources required to meet a targeted production rate and the tasks to be assigned to each of these resources using a technique called line balancing.
GT layouts are designed with the objective of sub-dividing a universe of machines and components into sub-groups such that each sub-group consists of part families and machine groups.
New technology manufacturing such as Flexible Manufacturing Systems (FMS) have the potential to simplify flow complexities in mid-volume, mid-variety manufacturing organizations due to increased flexibility.
Volume, variety & flow characteristics determine the complexity of operations management. By a careful design of the process, some of the complexities can be minimized.