## Slide 1: Supplement 10A
Simulation Modelling

## Slide 2: Improving a Banking System Problem context
Consider a branch of the State Bank of India in a centrally located place that has observed an increase in the waiting time of the customers
We want to understand the impact of alternative operational choices to address this problem:
  Adding two more counters
  Increasing the service rate by deploying some technology choices
  Adding some waiting spaces and
  Resorting to other mechanisms of reducing the demand placed on the servers
In order to analyze these alternatives we need to build a model of the system and study its behavior with respect to key performance metrics such as waiting time

## Slide 3: Modelling complexities in this problem
The bank in reality will cater to a variety of customers including
  the retail customer having a personal savings bank account in the branch,
  the small and medium business customers and
  the large industrial clients.
There will be multiple counters with random fluctuations in arrival and service patterns
  Significant variations in the arrival patterns of the customers into the branch not only during the working hours on a particular day but also across calendar days
  Behavioral patterns of the service providers in the branch will vary across counters and time
Due to these, the operation system is likely to be much more complex than what the available queueing models can solve

## Slide 4: Why Simulation Modelling?
Several operations management problems do not lend themselves to modeling and analysis using available simple mathematical models
  Banking example (discussed previously)
  In the traffic and capacity problem in a supermarket, using the simple single server queue with steady-state condition may not truly reflect the working conditions of the supermarket.
  Study of realistic situations requires complex modeling techniques that not only makes the modeling effort difficult but also often times results in intractable solutions
Simulation is a well-known method developed during the Second World War time which enables an operations manager to model complex real-life situations and obtain some insights

## Slide 5: What is simulation?
A mechanism in which a numerical model is built in which the reality is mimicked.
By repeated use of the numerical model it is possible to obtain some insights about the behavior of the system and use this information to make certain choices about the operating system.

## Slide 6: When to use simulation?
A simulation model is often resorted to under the following conditions:
  When the system to be studied does not lend itself to any readily available mathematical model
  Mathematical models are available to study the system, however there are no known solution methodology's to derive some insights
  A complex set of random events tend to affect the behavior of the system and therefore it requires some stochastic analysis of the problem
  Existing solution methodologies are too expensive

## Slide 7: Simulation model Building blocks
A clock to keep track of the passage of time in which the behavior of the system is observed.
  In several occasions the clock is used to stop terminate the simulation
  Simulations are normally terminated either by the number of arrivals or the absolute value of the clock
A random number generator to sample random numbers and use them to incorporate certain stochastic elements of the system being studied
Mechanisms to collect data of interest as the clock advances from time zero to the end time

## Slide 8: Simulation of a single server queueing system
Inter Arrival Time (IAT) (min) | Probability | Cumulative Probability
3 | 10% | 10%
4 | 22% | 32%
5 | 11% | 43%
6 | 12% | 55%
7 | 15% | 70%
8 | 12% | 82%
9 | 11% | 93%
10 | 7% | 100%
Arrival time distribution
Customer No | Random Number Sampled | Time between arrivals | Clock (Arrival)
1 |  |  | 0
2 | 0.09 | 3 | 3
3 | 0.61 | 7 | 10
4 | 0.03 | 3 | 13
5 | 0.87 | 9 | 22
6 | 0.96 | 10 | 32
7 | 0.51 | 6 | 38
8 | 0.81 | 8 | 46
9 | 0.72 | 8 | 54
10 | 0.77 | 8 | 62
11 | 0.56 | 7 | 69
12 | 0.04 | 3 | 72
13 | 0.74 | 8 | 80
14 | 0.26 | 4 | 84
15 | 0.12 | 4 | 88
16 | 0.60 | 7 | 95
17 | 0.39 | 5 | 100
18 | 0.54 | 6 | 106
19 | 0.64 | 7 | 113
20 | 0.36 | 5 | 118
Generating the first 20 arrivals using a random number generator
Similarly one can generate the service times also using a distribution

## Slide 9: Simulation of a single server Queueing System
Customer No | Random Number | Time between arrivals | Clock (Arrival) | Service Time | Waiting time | Service Begin | Service Duration | Service End | Time in System | Clerk Idle
1 |  |  | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
2 | 0.09 | 3 | 3 | 4 | 0 | 3 | 4 | 7 | 4 | 2
3 | 0.61 | 7 | 10 | 4 | 0 | 10 | 4 | 14 | 4 | 3
4 | 0.03 | 3 | 13 | 2 | 1 | 14 | 2 | 16 | 3 | 0
5 | 0.87 | 9 | 22 | 1 | 0 | 22 | 1 | 23 | 1 | 6
6 | 0.96 | 10 | 32 | 5 | 0 | 32 | 5 | 37 | 5 | 9
7 | 0.51 | 6 | 38 | 4 | 0 | 38 | 4 | 42 | 4 | 1
8 | 0.81 | 8 | 46 | 6 | 0 | 46 | 6 | 52 | 6 | 4
9 | 0.72 | 8 | 54 | 1 | 0 | 54 | 1 | 55 | 1 | 2
10 | 0.77 | 8 | 62 | 3 | 0 | 62 | 3 | 65 | 3 | 7
11 | 0.56 | 7 | 69 | 5 | 0 | 69 | 5 | 74 | 5 | 4
12 | 0.04 | 3 | 72 | 5 | 2 | 74 | 5 | 79 | 7 | 0
13 | 0.74 | 8 | 80 | 3 | 0 | 80 | 3 | 83 | 3 | 1
14 | 0.26 | 4 | 84 | 6 | 0 | 84 | 6 | 90 | 6 | 1
15 | 0.12 | 4 | 88 | 1 | 2 | 90 | 1 | 91 | 3 | 0
16 | 0.60 | 7 | 95 | 1 | 0 | 95 | 1 | 96 | 1 | 4
17 | 0.39 | 5 | 100 | 6 | 0 | 100 | 6 | 106 | 6 | 4
18 | 0.54 | 6 | 106 | 1 | 0 | 106 | 1 | 107 | 1 | 0
19 | 0.64 | 7 | 113 | 2 | 0 | 113 | 2 | 115 | 2 | 6
20 | 0.36 | 5 | 118 | 2 | 0 | 118 | 2 | 120 | 2 | 3
 |  |  | Total |  | 5 |  |  |  | 68 | 57
Arrival times are as per the table shown in the previous slide
Service time distribution not shown explicitly here

## Slide 10: Single server queueing system Simulation results
In all, the total time of simulation for the 20 arrivals is 120 minutes as evident from the clock time of the exit of the last arrival
The cumulative waiting time in the system is 5 minutes
  Average waiting time is 5/20 = 0.25 min (15 secs)
The 20 arrivals together have spent 68 minutes in the system in order to get their service
  Average waiting time is 68/20 = 3.4 minutes
The total ideal time of the service provider at the service counter is 57 minutes
  Server utilization = (120 – 57)/120 = 52.5%

## Slide 11: News Vendor problem Simulation
Demand | Good | Fair | Poor
40 | 3% | 10% | 44%
50 | 5% | 18% | 22%
60 | 15% | 40% | 16%
70 | 20% | 20% | 12%
80 | 35% | 8% | 6%
90 | 15% | 4% | 
100 | 7% |  | 
Likely demand on a given day
Poor demand - 20%
Good demand – 35%
Fair demand – 45%
Type of the day
Buys a copy at Rs. 0.33
Sells it at Rs. 0.50.
Salvage value is Rs. 0.05
Costs, Revenues
Decision the newspaper boy faces is the number of papers that he needs to buy daily

## Slide 12: Cumulative Distribution of the demand related to the type of the day
Demand | Good | Cum. Probability | Fair | Cum. Probability | Poor | Cum. Probability
40 | 3% | 0.03 | 10% | 0.10 | 44% | 0.44
50 | 5% | 0.08 | 18% | 0.28 | 22% | 0.66
60 | 15% | 0.23 | 40% | 0.68 | 16% | 0.82
70 | 20% | 0.43 | 20% | 0.88 | 12% | 0.94
80 | 35% | 0.78 | 8% | 0.96 | 6% | 1.00
90 | 15% | 0.93 | 4% | 1.00 |  | 
100 | 7% | 1.00 |  |  |  | 

## Slide 13: New Vendor Problem Steps in the simulation
Fix the decision variable whose effect on the system needs to be studied. In the table below the effect of buying 60 newspapers every day is being studied.
Sample random number from the random number generator and use it for deciding the type of the day using their cumulative distribution table for the type of the day
Sample another random number from the random number generator and use it for deciding the demand expected using the community distribution of demand for the type of the day
Since the number of copies bought is known as well as the demand calculate the revenue for the day, last profit if any, salvage if any and the daily profit (if any)
This completes one day of simulation.
Repeat the above steps as long as the terminating condition for the simulation is achieved. In our example the above steps are performed 20 times and the statistics is used to assess their impact on the system.

## Slide 14: Results of the Simulation
Amount bought |  | 60.00 |  |  |  |  |  | 
Day | RND | Day type | RND | Demand | Revenue | Lost profit | Salvage | Daily profit
1 | 94 | Poor | 80 | 60 | 30.00 | 0.00 | 0.00 | 10.20
2 | 77 | Fair | 20 | 50 | 25.00 | 0.00 | 0.50 | 5.70
3 | 49 | Fair | 15 | 50 | 25.00 | 0.00 | 0.50 | 5.70
4 | 45 | Fair | 88 | 70 | 30.00 | 1.70 | 0.00 | 8.50
5 | 43 | Fair | 98 | 90 | 30.00 | 5.10 | 0.00 | 5.10
6 | 32 | Good | 65 | 80 | 30.00 | 3.40 | 0.00 | 6.80
7 | 49 | Fair | 86 | 70 | 30.00 | 1.70 | 0.00 | 8.50
8 | 0 | Poor | 73 | 60 | 30.00 | 0.00 | 0.00 | 10.20
9 | 16 | Good | 24 | 70 | 30.00 | 1.70 | 0.00 | 8.50
10 | 24 | Good | 60 | 80 | 30.00 | 3.40 | 0.00 | 6.80
11 | 31 | Good | 60 | 80 | 30.00 | 3.40 | 0.00 | 6.80
12 | 14 | Good | 29 | 70 | 30.00 | 1.70 | 0.00 | 8.50
13 | 41 | Fair | 18 | 50 | 25.00 | 0.00 | 0.50 | 5.70
14 | 61 | Fair | 90 | 80 | 30.00 | 3.40 | 0.00 | 6.80
15 | 85 | Poor | 93 | 70 | 30.00 | 1.70 | 0.00 | 8.50
16 | 8 | Good | 73 | 80 | 30.00 | 3.40 | 0.00 | 6.80
17 | 15 | Good | 21 | 60 | 30.00 | 0.00 | 0.00 | 10.20
18 | 97 | Poor | 45 | 50 | 25.00 | 0.00 | 0.50 | 5.70
19 | 52 | Fair | 76 | 70 | 30.00 | 1.70 | 0.00 | 8.50
20 | 78 | Fair | 96 | 80 | 30.00 | 3.40 | 0.00 | 6.80
 |  |  | Total |  | 580.00 | 35.70 | 2.00 | 150.30
 |  |  | Average |  | 29.00 | 1.79 | 0.10 | 7.52

## Slide 15: Analyzing Multiple Decision Options
No. of newspapers bought | Average Daily Revenue (Rs) | Average Daily Profit (Rs)
40 | 20.00 | 1.96
50 | 25.00 | 5.36
60 | 29.00 | 7.52
70 | 32.25 | 8.75
80 | 34.00 | 8.12
90 | 34.25 | 5.63
100 | 34.25 | 2.83
By buying 70 newspapers daily the news vendor can maximize his/her daily profit.
On the other hand, by buying 90 or more number of newspapers that daily revenue flattens at Rs. 34.25 while the daily profit deteriorates.

## Slide 16: Simulation Modelling Steps
Problem Definition
Model Formulation
Data Preparation
Model Building
Model Validation
Strategic Planning
Tactical
Planning
Running Simulation
Analysis of Results
Document
Implement
Not
useful
Useful
Good
Bad

## Slide 17: Applications of Simulation
Capacity analysis: Use of capacity in operations often involves complex network of queues and several random behaviors of system entities.
Layout design: Design of manufacturing systems requires analysis with respect to number of resources to be deployed, utilization of resources, & their impact on waiting time, inventory buildup and congestion in the shop floor
Operational performance of service systems: Service systems are characterized by high levels of heterogeneity and complexity. Service systems also often present a complex network of queues.
Traffic management system: Study of traffic management systems involve real-time & dynamic aspects of congestion, queuing and waiting time
Supply-chain management: Several aspects of supply-chain require understanding of dynamic situations in order to address fleet management, logistics and distribution systems

## Slide 18: Simulation Modelling Chapter Highlights…
Simulation is a mechanism in which a numerical model is to mimic the reality.
A simulation model is often resorted to when the system to be studied does not lend itself to any readily available mathematical model or when a complex set of random events tend to affect the behavior of the system.
Building a simulation model will invariably utilize
  a clock to keep track of the passage of time in which the behavior of the system is observed
  a random number generator to sample random numbers and mechanisms to collect data of interest as the clock advances from time zero to the end time
Central to the simulation methodology is the use of random numbers to model the stochastic behavior that we face in real life in several operations systems.

## Slide 19: Simulation Modelling Chapter Highlights…
The variance introduced on account of using one set of random number needs to be eliminated before the results of a simulation study are used for meaningful interpretation. This is known as tactical planning of a simulation experiment.
Owing to its popularity a number of computer packages are available for simulation study of operations systems.
  The popular among them include ARENA, PROMODEL, @RISK, WITNESS and GPSS/H.
Simulation modeling finds a host of applications in operations management. Some of them are
  Capacity analysis,
  Layout design,
  Operational performance of service systems,
  Traffic management system and Supply-chain management