## Slide 1: Chapter 17
Inventory Planning and Control

## Slide 2: Inventory Planning Independent demand items
Finished goods and spare parts typically belong to independent demand items in manufacturing organisations
Two attributes characterise and distinguish independent demand items:
  Timing of demand: Independent demand items have a continuous demand
  Uncertainty of demand: There is considerable element of uncertainty in the demand in the case of independent demand items
Inventory planning of independent demand items must address the following two key questions:
  How much?
  When?

## Slide 3: Types of Inventory
Seasonal Inventory: Seasonality in demand is absorbed using inventory
Decoupling Inventory: Complexity of production control is reduced by splitting manufacturing into stages and maintaining inventory between these stages
Cyclic Inventory: Periodic replenishment causes cyclic inventory
Pipeline Inventory: Exists due to lead time
Safety Stock: Used to absorb fluctuations in demand due to uncertainty

## Slide 4: Decoupling Inventory An illustration
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
Stage 2
Stage 1
Stage 3
Decoupling Inventory
Production System without any decoupling inventory

## Slide 5: Cyclic, Pipeline and Safety Stocks A graphical illustration
Quantity
Time
Safety stock
Cyclic Stock
Pipeline inventory
L
Cyclic inventory, pipeline inventory and safety stocks are critically linked to “how much” and “when” decisions in inventory planning

## Slide 6: Costs in Inventory Planning Carrying Cost
Interest for short-term borrowals for working capital
Cost of stores and warehousing
Administrative costs related to maintaining and accounting for inventory
Insurance costs, cost of obsolescence, pilferage, damages and wastage
All these costs are directly related to the level of inventory

## Slide 7: Computation of Carrying Cost An illustration
Sl. No. | Item of Expenditure (Annual) | Amount (₹)
1 | Stationary | 75,000.00
2 | Insurance premium | 375,000.00
3 | Establishment expenses & Overheads | 275,000.00
4 | Salary of Stores Personnel | 1,100,000.00
 | Total expenditure | 1,750,000.00
 | Average Value of the inventory in Stores | 35,000,000.00
 | Warehousing cost (in % inventory value) | 5.00%
a | Cost of warehousing | 5.00%
b | Cost of capital (assumed) | 15.00%
c | Obsolescence (estimated historically) | 2.00%
d | Damages, spoilage etc. (estimated historically) | 1.00%
 | Carrying cost (%) | 23.00%

## Slide 8: Costs in Inventory Planning Ordering Cost
Search and identification of appropriate sources of supply
Price negotiation, contracting and purchase order generation
Follow-up and receipt of material
Eventual stocking in the stores after necessary accounting and verification
A larger order quantity will require less number of orders to meet a known demand & vice versa
Cost of carrying and cost of ordering are fundamentally two opposing cost structures in inventory planning

## Slide 9: Computation of Ordering Cost An illustration
Sl. No. | Item of Expenditure (Annual) | Amount (₹)
1 | Stationary | 80,000.00
2 | Telephone | 40,000.00
3 | Other communication Expenses | 60,000.00
4 | Salary of Purchase Department Personnel | 1,100,000.00
5 | Inwards Goods Inspection Section Expenses | 350,000.00
6 | Other expenses & Overheads | 200,000.00
 | Total Expenditure | 1,830,000.00
 | No. of purchase orders generated | 600.00
 | Average Cost of Ordering | 3,050.00

## Slide 10: Costs in Inventory Planning Shortage Cost
Costs arising out of pushing the order back and rescheduling the production system to accommodate these changes
Rush purchases, uneven utilisation of available resources and lower capacity utilisation
Missed delivery schedules leading to customer dissatisfaction and loss of good will
The effects of shortage are vastly intangible, it is indeed difficult to accurately estimate

## Slide 11: Inventory Control for deterministic demand: EOQ Model
Demand during the planning period = D
Order quantity = Q
The cost of ordering per order =
Inventory carrying cost per unit per unit time =
The total ordering cost is given by
The average inventory carried by an organisation=
The cost associated with carrying inventory =
Total cost of the plan =
Total cost of carrying inventory + Total cost of ordering
TC(Q) = +

## Slide 12: Inventory Control for deterministic demand: EOQ Model…
When the total cost is minimum, we obtain the most economic order quantity (EOQ). By taking the first derivative of with respect to Q and equating it to zero we can obtain the EOQ
Differentiating total cost equation with respect to Q we obtain,
The second derivative is positive and hence we obtain the minimum cost by equating the first derivative to zero.
Denoting EOQ by Q*, we obtain the expression of Q* as:
The optimal number of orders =
Time between orders =

## Slide 13: EOQ Model A graphical representation
Total cost of carrying
Total cost of ordering
Sum of the two costs
Minimum Cost
Economic
Order Qty.
Level of Inventory
Cost of Inventory

## Slide 14: Issues in using EOQ Model Model assumptions
The demand is known with certainty
Demand is continuous over time
There is an instantaneous replenishment of items
The items are sourced from an outside supplier
Assumptions about order quantity
  There are no restrictions in the quantity that we can order
  There are no preferred order quantities for the items
  No price discount is offered when the order size is large
Despite this, the EOQ model could be applied with suitable modifications because it is robust
Assumptions 3, 4 and 5 can be addressed with required modifications
Relaxing assumption 1 will result in shortages due to difficulty in estimating demand

## Slide 15: Estimation of Safety Stock From empirical Data – An example
Demand during LT | Frequency | Demand Exceeding Lower Class | 
 |  | Cumulative Frequency | Cumulative Percentage
0-30 | 2 | 114 | 100.00%
31-60 | 5 | 112 | 98.25%
61-90 | 11 | 107 | 93.86%
91-120 | 20 | 96 | 84.21%
121-150 | 25 | 76 | 66.67%
151-180 | 30 | 51 | 44.74%
181-210 | 13 | 21 | 18.42%
211-240 | 5 | 8 | 7.02%
241-270 | 2 | 3 | 2.63%
271-300 | 1 | 1 | 0.88%
300 - | - | - | -

## Slide 16: Frequency Ogave of weekly demand

## Slide 17: What is the right safety stock?
Avg. demand during LT = 143
For 90% service level
  Demand = 203
  Safety stock = 203 - 143= 60
For 95 % service level
  Demand = 224
  Additional Safety stock (over the 90% service level) = 224 - 203 = 21

## Slide 18: Computing safety stock Using Normal Distribution
Let the demand during lead time
follow a Normal distribution
Standard normal variate corresponding to an area of covered on the left side of the normal curve =
,
Mean demand during lead-time =
Standard deviation of
demand during lead-time =
Desired service level =
The probability of a stock out =
Safety stock (SS) is given by SS =

## Slide 19: Continuous Review (Q) System An illustration
ROP
SS
Q
L
Inventory Level
Time
Safety Stock
Mean Demand during LT
Inventory Position
Physical Inventory

## Slide 20: Periodic Review (P) System An illustration
SS
L
Inventory Level
Time
Safety Stock
Inventory Position
Physical Inventory
R
2R
3R
QR
Q2R
Q3R
Order Up to Level
S

## Slide 21: Periodic & Continuous Review Systems: A comparison
Criterion | Continuous Review (Q) System | Periodic Review (P) System
How much to order | Fixed order qty: Q | S = μ(L+R) + Zα × σ(L+R) QR = S – IR
When to order | ROP = μ(L) + Zα×σ(L) | Every R periods
Safety stock | SS = Zα×σ(L) | SS = Zα×σ(L+R)
Salient aspects | Implemented using two bin system Suited for medium and low value items | More safety stock More responsive to demand Ease of implementation

## Slide 22: Inventory Planning Models Example 17.5.(EOQ)
Mean of weekly demand : 200
Standard deviation of weekly demand : 40
Unit cost of the raw material : Rs. 300/-
Ordering cost : Rs. 460/- per order
Carrying cost percentage : 20% per annum
Lead time for procurement : 2 weeks
EOQ Model
Weekly demand = 200
Number of weeks per year = 52
Annual demand, D = 200*52 = 10,400
Carrying cost, Cc = Rs. 60.00 per unit per year
Economic Order Quantity =
Time between orders =

## Slide 23: Inventory Planning Models Example 17.5. (Q System)
Standard deviation of demand during L,
=
ROP =
+
= 400 + 93 = 493
Q System
Standard deviation of weekly demand = 40
Lead time, L = 2 weeks
Mean demand during L,
= 2* 200 = 400
For a service level of 95%, SS =
= 1.645*56.57 = 93.05
93
Using EOQ as the fixed order quantity, Q system can be designed as follows: As the inventory level in the system reaches 493, place an order for 400 units. This will ensure in the long run a service level of 95%.

## Slide 24: Inventory Planning Models Example 17.5. (P System)
Using the time between orders derived from the EOQ model as the basis for review period
Review period, R = 2 weeks
Mean demand during (L + R),
= 200*(2 + 2) = 800
For a service level of 95%,
Order up to level, S =
+
= 800 + 132 = 932
= 1.645*80 = 131.6
132
SS =
=
Standard deviation of demand during (L + R),
P System
The P system can be designed as follows: The inventory level in the system is reviewed every two weeks and an order is placed to restore the inventory level back to 932 units. This will ensure a service level of 95%.

## Slide 25: Selective Control of Inventories Alternative Classification Schemes
ABC Classification (on the basis of consumption value)
XYZ Classification (on the basis of unit cost of the item)
  High Unit cost (X Class item)
  Medium Unit cost (Y Class item)
  Low unit cost (Z Class item)
FSN Classification (on the basis of movement of inventory)
  Fast Moving
  Slow Moving
  Non-moving
VED Classification (on the basis of criticality of items)
  Vital
  Essential
  Desirable
On the basis of sources of supply
  Imported
  Indigenous (National Suppliers)
  Indigenous (Local Suppliers)

## Slide 26: ABC Classification A graphical illustration

## Slide 27: Inventory Planning for Single Period Demand
Let Co = Cost of over stocking per unit
Cu = Cost of under stocking per unit
Q = Optimal number of units to be stocked
d = Single period demand
= The probability of the single period demand being at most Q units

## Slide 28: Single Period Demand Model Example 17.6.
Selling price per box of the item : Rs. 1300.00
Cost of production : Rs. 1000.00
Cost of under stocking, Cus : Rs. 300.00
Salvage value : Rs. 800.00
Cost of over stocking, Cos : Rs. 200.00
As per equation 18.11, the optimal quantity to stock is obtained as:
On examination of the cumulative probability values in the last column of the demand table, a value of Q = 300 satisfies this requirement. Therefore, the manufacturer should plan for an inventory of 300 boxes for sale during the festival

## Slide 29: Inventory Planning & Control Chapter Highlights
Every organization carries five different types of inventory:
  Cyclic stock, Pipeline inventory, Safety stock, Decoupling inventory, Seasonal inventory.
Inventory planning is done in order to minimize the total cost of the plan. The costs include
  Cost of carrying inventory
  Cost of ordering
  Cost of shortages
The key decisions in any inventory planning scenario is to answer the “how much” and the “when” questions.
The EOQ model is useful for inventory planning in the case of multi-period deterministic demand situations.

## Slide 30: Inventory Planning & Control Chapter Highlights…
The EOQ model is robust to model parameters and could be suitably modified to incorporate some real life situations such as quantity discounts and non-zero lead time for supply.
Service level is a useful concept for modeling inventory planning in the case of stochastic demand. Safety stocks can be built commensurate to the desired service level.
A fixed order quantity (Q system) or continuous review system of inventory planning and control is useful for B class and C class items of inventory.
  A popular application of the continuous review system in organizations is the two-bin system.

## Slide 31: Inventory Planning & Control Chapter Highlights…
A fixed order interval or a periodic review system (P system) is useful for planning and control of high value and A class items.
  The P system is more responsive to changes in demand patterns than the Q system.
Selective control of inventories is achieved through alternative classification methodologies. The ABC, VED and XYZ classifications are often used by organizations
The news vendor model is useful for inventory planning in the case of single period demand