## Slide 1: Chapter 19
Six-Sigma Quality Control

## Slide 2: Six Sigma Approach to Quality
Six sigma is a new approach to process control first practiced by companies such as General Electric and Motorola to achieve near zero defects in processes
Elements of six-sigma
  Understanding customer needs well
  Appropriate and disciplined use of data and statistical tools
  Statistical analysis and a closer attention to managing and improving business processes using a set of tools

## Slide 3: How is it different from traditional approach?
A new metric, Defects Per Million Opportunities, to predict/assess the quality of a business process
A new methodology, DMAIC (Define-Measure-Analyze-Improve-Control), to ensure that very high levels of quality could be assured in the chosen business processes thereby generating favourable outcomes to both the business and the customers
An organizational framework for ensuring the above outcomes are generated on a sustained basis

## Slide 4: Defects Per Million Opportunities (DPMO)
It indicates how many defects a process generates in a million opportunities
  While service industries find it convenient to use DPMO, manufacturing organizations use Parts Per Million (PPM). Both are conceptually same.
If in a process
  “k” Denotes the number of opportunities for making a defect per unit of execution of that process
  “n” Number of units of observation of the process
  “d” Number of defects that occurred in that process during the observation
  The defects per opportunity =

## Slide 5: DMAIC Methodology
Chart: 
 | 20 | 20 | 20 | 20 | 20
Define
Measure
Analyze
Improve
Control

## Slide 6: DMAIC Methodology
Define
  Define the problem, the requirements, project scope, project charter
  Set goals for improvement
Measure
  Identify variables to be measured, the type of measurement
  Data collection and synthesis
Analyze
  Develop a set of tools for analysis
  Apply graphical tools of analysis
  Identify possible sources of variation and “vital” few root causes
  Explore means of eliminating them

## Slide 7: DMAIC Methodology
Improve
  Generating and validating improvement alternatives
  Creating new process maps for the process
Control
  Develop control plan
  Establish revised standard measures to maintain performance
  Develop relevant raining plans to maintain standards

## Slide 8: Organization for six sigma
Process Owner
  Supervisor or a manager who takes responsibility for various steps of a process that is responsible for delivering some output to the customer. It could be the in a particular work area where the improvement project has been identified
Team Leader & Members
  Team leader (the project leader) and the members will comprise of the employees in the chosen work area
  They will have day-to-day operational control of activities
In six sigma, three terminologies are used to indicate these organizational entities. This includes Master Black Belt, Black Belt and Green Belt. The depth of training and experience differentiates these three.

## Slide 9: Organization for six sigma
Six sigma coach
  A consultant or a senior person in the organization who offers expert knowledge on various aspects of six sigma.
  This includes statistical tools, process design & analysis, change management, small group improvement, use of QC tools for improvement etc.
Sponsor
  A member of the senior management who oversees the overall progress and implementation
  Helps the team refine the project scope, sorts out issues cutting across other parts of the organization, approves projects and provides the necessary support in terms of resources

## Slide 10: Statistical Process Control
Collective set of tools & techniques used to develop a quality assurance system when business processes exhibit variations is known as Statistical Process Control (SPC)
Key issues addressed in SPC based quality assurance system:
  How does one ensure that the random events are indeed rare events?
  How do we know whether the observed changes are due to random variations or assignable causes?

## Slide 11: Common & Assignable Causes
Two types of variations occur in business processes
  Chance variations due to common causes
    Common causes are those due to random events that cannot be controlled
  Non-random variations due to assignable causes
    When observed variations are not statistically found to be due to random events, it clearly points to the existence of assignable causes
      Errors due to operator skill level differences
      Changes in the operating condition of an equipment
      Changes introduced in the standard operating procedures
In the case of assignable causes, the system will drift from desired level of performance over time

## Slide 12: Quality Assurance using SPC Some terminologies
Designed Standard
Centre of specification limits (Target)
Upper Specification Limit (USL)
Lower Specification Limit (LSL)
(USL – LSL): Desired Tolerance for the specs.
This represents the voice of the customer
Status of process
Centre of the process (Process Average)
Upper Control Limit (UCL)
Lower Control Limit (LCL)
(UCL – LCL): Spread of the process
This represents the voice of the process

## Slide 13: Control Chart A generalised representation
Process Average
Upper Control Limit (UCL)
Lower Control Limit (LCL)
Plot of sample data

## Slide 14: Setting up a process control system
Choose the characteristic
for process control
Choose the
Measurement method
Choose an appropriate
Sampling procedure
Choose the type of
Control Chart
Calculate
control limits
Plot the data & Analyse

## Slide 15: Characteristics for process control Some examples
Sl. No. | Type of Applications | Characteristic for Measurement
1 | Component Manufacturing | Conformance of physical measurements of components and sub-assemblies to specifications Conformance to operating characteristics of machines and other resources involved in the process
2 | Final Assembly | Number of defects in the product Conformance to test specifications Number of missing elements
3 | Process Industries | Temperature, Pressure and Heat specifications Conformance to product specifications Conformance to equipment specifications Vibrations and other variations in equipments and sub-systems Conformance to specifications of the automation & control system
4 | Service Systems | Number of defects in various business processes Errors in processing documents Conformance to waiting time/lead time related specifications

## Slide 16: Choosing a characteristic Examples from service industry
How long does it take to complete the patient admission process in a hospital?
How dissatisfied were the customers when they stayed in a hotel for a holiday?
Does our process of understanding customer requirements needs improvement?
How capable are my sub-processes in software development?

## Slide 17: Measurement Methods
Attribute Based
  simple clustering of the characteristic into a few categories (such as good or bad)
  Two frequently used attribute measures are:
    Proportion of defects (denoted as p)
    Number of defects (denoted as c)
  measurements are easy to make, quick & less expensive, but reveal very little information about the process
Variable Based
  Detailed observation of the characteristic (such as length, diameter, weight)
  measurement will be expensive and more time consuming but will provide a wealth of information about the process

## Slide 18: Types of Control Charts
Variable based control chart
  X bar and R Charts
Attribute based control chart
  P chart
  C chart

## Slide 19: Notations for control charts

## Slide 20: X bar and R Chart Setting control limits

## Slide 21: Coefficients for computing LCL and UCL in X-bar and R charts*
Source: Juran, J.M. and F.M. Gryna, (1995), “Quality Planning and Analysis”, Tata McGraw-Hill, 3rd Edition, New Delhi, pp 385.

## Slide 22: X bar Chart An example

## Slide 23: R Chart An example

## Slide 24: P chart Setting the control limits

## Slide 25: P Chart An example

## Slide 26: C Chart Setting up the control limits

## Slide 27: C Chart An example (with an outlier)

## Slide 28: C Chart Is this process behaving normally?

## Slide 29: When to stop the process? 15 points in a row in Zone C
Zone A
Zone A
Zone C
Zone B
Zone C
Zone B
+1
+2
+3
-3
-2
-1

## Slide 30: When to stop the process? 14 points in a row alternating up and down
Zone A
Zone A
Zone C
Zone B
Zone C
Zone B
+1
+2
+3
-3
-2
-1

## Slide 31: When to stop the process? Additional rules
One point beyond Zone A
Nine points in a row in Zone C or beyond
Six points in a row, steadily increasing or decreasing
Fourteen points in a row, alternating up and down
Two out of three points in a row in Zone A or beyond
Four out of five points in a row in Zone B and beyond
Fifteen points in a row in Zone C

## Slide 32: Predictive capability of processes Which process is better?
Spread of a process is indicative of its capability

## Slide 33: Predictive capability of processes Which process is better?
Chart: 
Target
LSL
USL
Process B
Process A
Offset
A process that is aligned closer to the desired target is likely to be more capable

## Slide 34: Process Capability
Process Capability is defined by the spread of the process
Potential capability (Cp) is defined as the ratio of the difference in specification limits to the process spread
Cp =
Actual capability (Cpk) takes into consideration the extent to which the process has deviated from the desired target
Cpk =

## Slide 35: Process Capability & Defects
Process Capability Index (Cpk) | Total Products outside two-sided specification limits
0.25 | 453,255 ppm
0.50 | 133,614 ppm
0.60 | 71,861 ppm
0.80 | 16,395 ppm
1.00 | 2,700 ppm
1.20 | 318 ppm
1.50 | 7 ppm
1.70 | 0.34 ppm
2.00 | 0.0018 ppm
Source: Quality Planning & Analysis, Juran & Gryna, Chapter 17, 3e

## Slide 36: Six sigma quality A graphical representation
Cp

## Slide 37: Acceptance Sampling
A method in which the decision with regard to acceptance or otherwise of a lot of incoming material is based on the observations made using a sample
Setting up a system for acceptance sampling requires addressing the following questions:
  What is the size of the sample required for assessing the quality?
  What should be the criteria for acceptance of the lot?
  Is it enough to have just one sample or is it desirable to go for multiple samples
  How do we assess the impact of the choice of the above parameters on the quality level in the long run?

## Slide 38: Sampling Plan
A sampling plan describes
  the Lot size (N)
  size of the sample to be assessed (n)
  the acceptance number (c): the number of defects permissible in the observed sample
Therefore, a single sampling plan is denoted by (N, n, c)
In the case of multiple sampling plans, for each of the plan, the sample size (n1, n2 etc.) and the acceptance number (c1, c2 etc.) needs to be specified

## Slide 39: Acceptance Sampling Operating Characteristics
Acceptable Quality Level (AQL): the percent defect that the buyer is willing to tolerate in the lot delivered by the supplier
Lot Tolerance Percent Defective (LTPD): the worst quality beyond which the manufacturer is not willing to accept the incoming lot
Producer’s risk: the risk supplier faces in getting his/her lot rejected when indeed it was conforming to the agreed terms
Consumer’s risk: the risk that a manufacturer faces of accepting a lot with poor quality beyond his/her tolerance level
Operating Characteristics (OC) Curve: A graphical representation of a sampling plan that reveals the above aspects of a sampling plan

## Slide 40: Operating Characteristics Curve Example 19.5
Consumer’s Risk
Producer’s Risk
OC Curve for n=500, c=2
AQL
LTPD

## Slide 41: Statistical Process Control Chapter Highlights
Six sigma is a new approach to process control based on as set of principles that enable organizations improve their quality to near zero defects level
Six sigma quality control differentiates itself from the traditional quality control methodology on the basis of three features:
  A new metric, Defects Per Million Opportunities, to predict/assess the quality of a business process,
  A new methodology, DMAIC (Define-Measure-Analyze-Improve-Control)
  An organizational framework for ensuring the above outcomes are generated on a sustained basis

## Slide 42: Statistical Process Control Chapter Highlights…
All processes exhibit variations on account of two causes
  Common causes of variations happen on account of random events
  Assignable causes introduce variations that can be detected and eliminated
Setting up a process control system involves
  choosing a characteristic to control
  identifying a measurement method and
  developing a relevant control chart
A plot of the data helps a quality manager to assess if the process is in control and also helps her to detect any impending shift in process parameters

## Slide 43: Statistical Process Control Chapter Highlights…
Superimposing the specification limits on the control chart helps an organisation to assess the process capability and the likely number of defects that the process will produce. It also helps to target for a six-sigma quality improvement programme.
Acceptance sampling is used to accept a lot of items based on the observed number of defects in the sample drawn out of the lot
The performance of an acceptance sampling plan could be judged by developing an Operating Characteristics (OC) curve for the plan
An acceptance sampling design results in a certain amount of risk for both the customer and supplier